## Slide 1: Sensor Fusion for NXP Microcontrollers – Part 1
Michael Stanley
NXP Sensors division

## Slide 2: Part 1 vs Part 2
Part 1 (This course) focuses on the mechanics of getting a sensor fusion application up and running
Part 2 deals with some of the theoretical underpinnings
This course focuses on the Version 7.xx Sensor Fusion Library

## Slide 3: Part 1 Agenda
Sensors 101
What is the sensor fusion library used for?
NXP Sensor Fusion Version 7.00
Supported hardware and how to get it
Sensor Fusion Toolbox for Windows
Sensor Fusion Toolbox for Android
Supported development tools and how to get them
Using the MCUXpresso Config Tools to generate a Version 7.xx sensor-fusion enabled SDK
Version 7.00 sensor fusion library structure
IDE Road Trip
Various Gory Details
Bare-Metal Implementation
Version 7.00 build process
Free-RTOS implementation
Fusion Standby Mode
Topics for another day

## Slide 4: Navigation Icons
Is used to flag places where “you get stuff”
Is used to point out places where you need to do something

## Slide 5: Documentation Included In The Sensor Fusion Kit
NXP Sensor Fusion User Guide
NXP Sensor Fusion Library for Kinetis Data Sheet
NXP AN5016, Trigonometry Approximations
NXP AN5017: Aerospace, Android and Windows 8 Coordinate Systems
NXP AN5018: Basic Kalman Filter Theory
NXP AN5019: Magnetic Calibration Algorithms
NXP AN5020: Determining Matrix Eigenvalues and Eigenvectors by Jacobi Algorithm
NXP AN5021: Calculation of Orientation Matrices from Sensor Data
NXP AN5022: Quaternion Algebra and Rotations
NXP AN5023: Sensor Fusion Kalman Filters
NXP AN5286: Rev. 2.0: Precision Accelerometer Calibrations

## Slide 6: Sensors 101

## Slide 7: An Accelerometer Measures Linear Acceleration Plus Gravity
+Y
+X
+Z
Accelerometer
An accelerometer by itself is a “3 axis” system
When any axis is vertical, we cannot
detect rotation about that axis

## Slide 8: What Do We Mean: Accelerometers Measure Linear Acceleration Plus Gravity?
When horizontal, and at rest:
X = 0
Y = 0
Z = 1g
When horizontal, and accelerating at 1g in the direction of the arrow:
X = 1g
Y = 0
Z = 1g

## Slide 9: Adding a Gyroscope
This “6 axis” system is known as an Inertial Measurement Unit or “IMU”
This is a Right Hand System (RHR)
+Y
+X
+Z
Accelerometer
ωz
ωx
ωy
Gyro
A 3-axis gyroscope measures angular velocity about each of the 3 axes.

## Slide 10: Adding a Magnetometer
+Y
+X
+Z = up
Accelerometer
ENU
= North
= East
Magnetometer
ωz
ωx
ωy
Gyro
This “9 axis” system is known as a magnetic, angular rate & gravity (MARG) sensor
Add a processor and you have an attitude & heading reference system (AHRS)
A 3-axis magnetometer gives you the X/Y/Z components of the magnetic field.

## Slide 11: As an Aside...
horizontal intensity = 23.4T
In Grapevine Texas, during the week of FTF2014, almost 2/3 of the earth’s magnetic field was directed DOWN

## Slide 12: Adding a Pressure Sensor
+Y
+X
+Z = up
Accelerometer
ENU
= North
= East
Magnetometer
Pressure
ωz
ωx
ωy
Gyro
This is a “10 axis” system
Pressure is a scalar (versus vector) quantity

## Slide 13: Pressure Can Give You An Estimate Of Altitude
Altitude = K1 X (1 - (P/P0)K2)
K1 = 44330.77 meters
K2 = 0.190263 (unitless)
P0 = 101325 Pascals

## Slide 14: Notice This Is A Log Scale...
Chart: Typical Sensor Power in W
| 12.5Hz LP Acc only | 400Hz LP Acc | 12.5Hz Mag | 400Hz Mag | Pedometer | Pressure (1Hz) | Hybrid Mag + Accel (200Hz) | Gyro Standby | Gyro RUN
 | 20 | 234 | 100 | 1437.5 | 151.2 | 662.5 | 1100 | 9500 | 14500
This chart was created 2013, you can expect numbers to decrease over time.

## Slide 15: Gyro ready to active = 2/ODR + 10ms
Chart: Typical Sensor Power in W
| 12.5Hz LP Acc only | 400Hz LP Acc | 12.5Hz Mag | 400Hz Mag | Pedometer | Pressure (1Hz) | Hybrid Mag + Accel (200Hz) | Gyro Standby | Gyro RUN
 | 20 | 234 | 100 | 1437.5 | 151.2 | 662.5 | 1100 | 9500 | 14500
Notice that the magnetometer currents are approximately 5X to 6X the accelerometer currents
Now Try A Linear Scale...

## Slide 16: Sensor Strengths & Weaknesses
Sensor | Strengths | Weaknesses
Accelerometer | Inexpensive Extremely low power Very linear Very low noise | Measures the sum of gravity and acceleration. We need them separate.
Magnetometer | The only sensor that can orient itself with regard to “North” Insensitive to linear acceleration | Subject to magnetic interference Not “spatially constant”
Gyro | Relatively independent of linear acceleration Can be used to “gyro-compensate” the magnetometer | Power hog Long startup time Zero rate offset drifts over time
Pressure Sensor | The only stand-alone sensor that can give an indication of altitude | Not well understood A “relative” measurement Subject to many interferences and environmental factors

## Slide 17: Additional Observations
Accelerometers are the most power efficient motion sensor you’ll find
They often include motion detection circuits – use those to power the system up/down for idle periods
Accelerometers are low power because they are usually “passive” devices. The proof mass moves only when the device is in motion
Gyros have continuously moving proof masses, requiring much higher currents to keep them in motion
TMR1-based magnetic sensors are arranged in a Wheatstone bridge formation – requiring DC biases
Another good sensor to “gate” others is an ambient light sensor
1 TMR = Tunneling MagnetoResistive

## Slide 18: Sensor Types Required As Function Of Algorithm
Algorithm | Sensor Fusion IfDef | Pressure | Accelerometer | Magnetometer | Gyro
Altitude | F_1DOF_P_BASIC | X |  |  | 
Tiltmeter | F_3DOF_G_BASIC |  | X |  | 
2D Automotive Compass | F_3DOF_B_BASIC |  |  | X | 
Rotation | F_3DOF_G_BASIC |  |  |  | X
Tilt Compensated Compass | F_6DOF_GB_BASIC |  | X | X | 
Gaming Handset | F_6DOF_GY_KALMAN |  | X |  | X
Gyro Stabilized Compass | F_9DOF_GBY_KALMAN |  | X | X | X

## Slide 19: What is the sensor fusion library used for?

## Slide 20: What Is The Sensor Fusion Library Used For?
The primary output of the sensor fusion library is device orientation relative to a global frame of reference
North
East
Up
Earth Frame
Body or Device Reference Frame
The device orientation can be defined as the rotation necessary to map the global frame of reference into alignment with the body frame of reference (or vice versa).

## Slide 21: Why Is This Important?
Orientation is required for:
Gaming
Toys
Augmented Reality
Navigation / Location Based Services
Motion Control
UAV stabilization
Robots
Segway
Gun sights
Surveying
Human body tracking
Air mouse / TV remote control
Optical Image Stabilization
Context aware applications

## Slide 22: Sensor Fusion Data Flow for Consumer Devices
3-Axis Acc
3-Axis Mag
3-Axis Gyro
Trim
Trim & Hard/Soft compensation
Trim
hi/low/band pass filtering
Kalman Filter or similar function
Geometric computations
Rotation matrix
Orientation (φ, Θ, Ψ)
hi/low/band pass filtering
hi/low/band pass filtering
Shake detection
Calculate hard/soft iron parameters
Acc x,y,z
ω x,y,z
B x,y,z
shake event
Tilt-compensated mag heading
Quaternion
Sensor Fusion
Raw data
calibration
parameters
FoR mapping
FoR mapping
FoR mapping
FoR = Frame of Reference Mapping
Pressure
Trim
hi/low/band pass filtering
Pressure
Sensor Hub Functions
Configure, Power State, Data Control

## Slide 23: NXP Sensor Fusion Version 7.00

## Slide 24: Version 5.00 Versus Version 7.xx
Feature | Version 5.00 | Version 7.xx
Supported Algorithms | 3-axis tilt from magnetometer or accelerometer, 3-axis gyro rotation, eCompass, accel + gyro gaming and full 9-axis NXP Magnetic Calibration | 
GUI Support | Sensor Fusion Toolbox for Windows Sensor Fusion Toolbox for Android | 
Packaging | Standalone | Bundled with the ISSDK, which is Integrated into the MCUXpresso SDK
Code Generator | Processor Expert | N/A
Toolsets | CodeWarrior Kinetis Design Studio | Kinetis Design Studio, IAR, ARM GCC, Atollic and (soon) MCUXpresso
Boards supported “out of the box” | KL25Z, KL26Z, KL46Z, K20D50M, K64F | K22F, K64F1
RTOS or Bare Metal | MQXLite only | FreeRTOS or Bare Metal
Magnetic Calibration | Separate background thread | Serialized to run in fusion thread
1 A KL25Z port is available on the community, and Mike has a private port for K66F

## Slide 25: Magnetic Calibration Tradeoffs Between V5.00 And V7.Xx Sensor Fusion
Feature | V5.00 and earlier | V7.00
Accuracy | Same algorithms used for both | 
Startup time | A few seconds | Slower if coefficients have to be computed every time. Instantaneous if NVM storage is used for pre-computed coefficients.
Implementation | Required background thread | Not even visible to most programmers

## Slide 26: Version 5.00 Versus Version 7.xx
Feature | Version 5.00 | Version 7.xx
Programmable sampling and fusion rates | YES | YES
3- Clause BSD license | YES | YES
Nonvolatile storage of Magnetic Calibration and Trim parameters | No | YES
Includes Precision Accelerometer Trim | No | YES
Lower power option available | No | YES
Support for sensor FIFOs and multi-rate sensor sampling | No | YES

## Slide 27: http://www.nxp.com/sensorfusion

## Slide 28: Community Support for Sensor Fusion
https://community.nxp.com/community/ sensors/sensorfusion

## Slide 29: Supported Hardware and how to get it

## Slide 30: Required Hardware for V7.00 Sensor Fusion
FRDM-K22F or FRDM-K64F
FRDM-STBC-AGM01 or FRDM-MULT2-B Sensor Shield
A USB to USB cable
A PC running Windows

## Slide 31: FRDM-STBC-AGM01 Sensor Shield

## Slide 32: FRDM-K22F Freedom Development Platform

## Slide 33: FRDM-K22F Features

## Slide 34: If You Have A FRDM-K64F

## Slide 35: Open SDA
MSD Bootloader
OpenSDA Application
OpenSDA MCU
Kinetis® K2x
Target
Processor
nRESET
UART RX/TX
SWD/JTAG
GPIO / ADC
UART TX/RX
SPI, GPIO
USB Host
IDE
File System
Serial Terminal
USB
GPIO
PWM
OpenSDA
“OpenSDA is a serial and debug adapter that is built into NXP® evaluation boards. It provides a bridge between your computer (or other USB host) and the embedded target processor, which can be used for debugging, flash programming, and serial communication, all over a simple USB cable.”

## Slide 36: OpenSDA Resources
http://nxp.com/opensda START HERE
https://www.segger.com/opensda.html
http://www.pemicro.com/opensda/
https://developer.mbed.org/handbook/Windows-serial-configuration
You must have Windows drivers installed to support your chosen implementation of OpenSDA. They can be obtained from the links above.
Each implementation varies in terms of supported features.
My personal preference is Segger’s, for speed of download, although it does lack drag and drop programming.

## Slide 37: http://www.nxp.com/freedom

## Slide 38: Sensor Fusion Toolbox for Windows

## Slide 39: Sensor Fusion Toolbox for Windows

## Slide 40: Put Your Board Flat On The Table When Starting Up

## Slide 41: Time To Wave The Board Around

## Slide 42: Now Have Magnetic Calibration

## Slide 43: Sensors Tab

## Slide 44: Dynamics Tab

## Slide 45: Kalman Filter Tab

## Slide 46: Magnetics Tab

## Slide 47: Precision Accelerometer Tab

## Slide 48: Precise Control Of Measurement Angles Is Only Required Once: Flat

## Slide 49: Inertial Navigations Systems Tab

## Slide 50: Sensor Fusion Toolbox for Android

## Slide 51: Sensor Fusion Toolbox for Android
Requires a FRDM-MULT2-B sensor shield or other Bluetooth adapter.

## Slide 52: Download it Using Google Play
Search for “Sensor Fusion”
Choose the version with the NXP Logo

## Slide 53: Navigating the Android GUI
The “Sources” Menu
The “Navigation” Menu
The “Options” Menu

## Slide 54: More Utility Functions
In-App Documentation
Setting Preferences

## Slide 55: If You Are Using A FRDM-MULT2-B Board
A
B
Make sure you check “Automatically enable Bluetooth on entry in the Preferences screen.
Make sure you have a jumper installed at “A”
The last few digits of the BlueRadios Bluetooth object name can be read on the module at “B”

## Slide 56: Sample Applications
Virtual room view responds to both board and phone orientations
Experiment with an air mouse / pointer

## Slide 57: Data Collection
Data Logging
Real-Time Statistics

## Slide 58: The Freescale Sensor Fusion Toolbox Features by Platform
Feature | Android | PC
Bluetooth wireless link |  | Requires BT on PC (built-in or dongle)
Ethernet wireless link | On WiGo board only | -
UART over USB | - | 1
OS requirements | >= Android 3.0 | >= Windows 7.0
Support for native sensors |  | -
Advanced Calibration | - | 
Device View |  | 
Panorama View |  | -
Statistics View |  | -
Canvas View |  | -
Orientation XY Plots | - | 
Inertial XY Plots | - | 
Magnetics | - | 
Kalman | - | 
Altimeter XY Plots | - | 
Data Logging Capability |  | 
Integrated documentation |  | 
Availability | Google Play | Freescale website
Price | Free | Free
1 FRDM_K64F and FRDM_K20D50M projects require a Processor Expert configuration change to run in wired mode.

## Slide 59: Using the MCUXpresso Config Tools to generate a Version 7.00 sensor-fusion enabled SDK

## Slide 60: Getting the KSDK - https://mcuxpresso.nxp.com

## Slide 61: Create a New Configuration

## Slide 62
Search for your board

## Slide 63
Click here and follow the prompts

## Slide 64: Hint
When you install your SDK, do not install it deep within a file hierarchy. Apparently KDS has problems with long path names.

## Slide 65: After Downloading And Expanding The SDK
Additional tool options are available when you configure the SDK download

## Slide 66: Supported development tools and how to get them

## Slide 67: http://www.nxp.com/mcuxpresso

## Slide 68: Kinetis Design Studio : http://www.nxp.com/kds

## Slide 69: When Invoking KDS, You Will Be Asked To Select A Workspace
Example pathname: <SDK root> /boards /frdmk22f_agm01 /issdk_examples /algorithms /sensorfusion

## Slide 70: Close The Welcome Screen

## Slide 71: File->Import->Existing Projects Into Workspace

## Slide 72: You Can Now Double Click On One Of The Projects To Open It.

## Slide 73: After Clicking The Hammer Icon To Build, You May Have A Few Warnings…

## Slide 74: Run->Debug Configurations
You need to tell KDS what OpenSDA implementation you are using.
Here, I am using Segger jlink

## Slide 75: Uncheck The “Enable SWO” Checkbox On The Startup Tab. Then Click The “Debug” Button

## Slide 76: Your Program Has Been Downloaded , Is Paused At The Start Of Execution And Is Ready To Run/Debug

## Slide 77: Version 7.xx sensor fusion library structure

## Slide 78
Application-specific bare metal or RTOS-based main()
install Sensor()
initialize Fusion Engine()
read Sensors()
runFusion()
initSensor FusionGlobals()
Status SubSystem
Control SubSystem
Board specific Hardware Abstraction Layer
KSDK = Kinetis Software Design Kit
NXP Sensor Fusion for Kinetis MCUs Verson 7.xx
NonVolatile Storage
Intelligent Sensor SDK
Sensor Fusion Core Functions
GPIO
UART
I2C / SPI
Flash Memory
The KSDK is available to main as well
condition Sensor Readings()

## Slide 79: Primary Subsystems and Associated Peripherals
Subsystem | Required | Peripherals Required | Comments
Main | Yes | Timer | PIT or similar if bare metal; SysTick commonly used for RTOS
Control | Debug minimum | UART | Example projects utilize two, one for OpenSDA wired connections, one for Bluetooth.
Status | No | Tri-Color LED | 
ISSDK | Yes | I2C and/or SPI | As required by the specific set of sensors used

## Slide 80: Example: FRDM-K64F And FRDM-FXS-MULT2-B / Peripheral Assignments
Subsystem | Function | Suggestion | Comments
Bare-metal main | Timer | PIT0 | Encapsulated in driver_pit.c/.h
FreeRTOS main | Timer | SysTick | Possible interaction with Sensor Toolbox metrics measurement
Control | UART | UART3 on PTC17:16 | Connects to Bluetooth module on sensor shields
 |  | UART0 on PTB17:16 | Connects to OpenSDA CDC (UART/USB) on the Freedom board
Status | Red LED | PTB22 | 
 | Green LED | PTE26 | 
ISSDK | I2C | I2C0 on PTC11:10 | All I2C sensors on FRDM-FXS-MULT2-B (excluding the FXLS8471Q)
 | Accel/Mag | FXOS8700 | I2C address 0x1E on the FRDM-FXS-MULT2-B
 | Gyro | FXAS21002 | I2C address 0x20 on the FRDM-FXS-MULT2-B
 | Altimeter | MPL3115A2 | I2C address 0x60 on the FRDM-FXS-MULT2-B

## Slide 81: Observations
The status and control subsystems are available to both the sensor fusion core and customer functions.
Everything is coded in C, but with a top level organization that could easily be recast into C++ in the future.
The sensor fusion core is (with the possible exception of some covariance numbers) completely hardware independent.
There are no low level procedural interfaces, you just look up sensor fusion outputs from standard global locations.

## Slide 82: IDE Road trip- Pause here to interactively review a project

## Slide 83: Sensor Fusion File Structure Within the SDK
SDK_2.1_FRDM-K22F-AGM01
boards
frdmk22f_agm01
Issdk_examples
algorithms
sensorfusion
frdm_k22f.c / .h
frdm_stbc_agm01_shield.h
Issdk_hal.h
middleware
Issdk_1.1
algorithms
sensorfusion
docs
sources
baremetal_agm01
freertos_agm01
build.h
FreeRTOSConfig.h

## Slide 84: Various gory details

## Slide 85: What To Look For In The Sources Directory
Filenames | Descriptions
approximations.c / .h | Contains custom trig functions optimized for performance
calibration_storage.c / .h | Functions for storing and retrieving trim parameters to/from flash
control.c / .h control_lpsci.c | The control subsystem – responsible for communicating with the Sensor Fusion Toolbox. control_lpsci.c is a custom version for the KL25Z low power UART.
debug.c / .h | Debug function in support of the Sensor Fusion Toolbox for Windows.
DecodeCommandBytes.c | Responsible for decoding serial command stream from the Sensor Fusion Toolbox.
driver_<objectName>.c / .h driver.h | sensor drivers, timer drivers. driver.h is a common header file for the sensors.
fusion.c / .h | The “hard core” sensor fusion routines
hal_frdm_fxs_mult2_b.c | Hardware abstraction layer for NXP sensor placement
magnetic.c / .h | The magnetic compensation sub-system
main_<>.c | A variety of example main()’s highlighting various options

## Slide 86: What To Look For In The Sources Directory
Filenames | Descriptions
matrix.c / .h | Generic matrix manipulation routines
motionCheck.c | Routine to implement low power check
orientation.c / .h | Routines for converting between various frames of reference
output_stream.h | The file responsible for streaming information to the Sensor Fusion toolbox
precisionAccelerometer.c / .h | The routines for implementing precision accelerometer trim
sensor_fusion .c / .h | The top level sensor fusion interface
standard_build.h | A standard project configuration file (an example of which should go into your project directory)
status.c / .h | The status subsystem (basically controls the LEDs)

## Slide 87: Examples of Other Important Files
Filenames | Descriptions
build.h | configures the Sensor Fusion build
frdm_k22f.c | Provides Arduino pin mapping
frdm_k22f.h | Defines for required peripheral pins, NVM locations
issdk_hal.h | Top level .h file for board hardware abstraction layer
frdm_stbc_agm01_shield.h | Sensor addresses and shield identifier
FreeRTOSConfig.h | FreeRTOS configuration file

## Slide 88
SensorFusionGlobals
ControlSubsystem *pControlSubsystem
StatusSubsystem *pStatusSubsystem
PhysicalSensor *pSensors
PressureSensor
AccelSensor
AccelCalibration
AccelBuffer
MagSensor
MagCalibration
MagBuffer
GyroSensor
SV_1DOF_P_BASIC
SV_3DOF_G_BASIC
SV_3DOF_B_BASIC
SV_3DOF_Y_BASIC
SV_6DOF_GB_BASIC
SV_6DOF_GY_KALMAN
SV_9DOF_GBY_KALMAN
miscellaneous individual parameters
miscellaneous function pointers
PhysicalSensor
PhysicalSensor *next
void *bus_driver
uint16_t type
uint16_t addr
uint16_t schedule
initializeSensor_t *initialize
readSensor_t *read
PhysicalSensor
PhysicalSensor *next
void *bus_driver
uint16_t type
uint16_t addr
uint16_t schedule
initializeSensor_t *initialize
readSensor_t *read
ControlSubsystem
miscellaneous individual parameters
miscellaneous function pointers
StatusSubsystem
miscellaneous individual parameters
miscellaneous function pointers

## Slide 89
Description | Data Type | Fusion algorithm option |  |  |  |  |  | SV_COMMON
 |  | G (accel) | B (auto compass) | Y (gyro) | GB (eCompass) | GY (accel + gyro) | GBY (9-axis) | 
roll in degrees | float | fLPPhi | fLPPhi | fPhi | fLPPhi | fPhiPl | fPhiPl | fPhi
pitch in degrees | float | fLPThe | fLPThe | fThe | fLPThe | fThePl | fThePl | fThe
yaw in degrees | float | fLPPsi | fLPPsi | fPsi | fLPPsi | fPsiPl | fPsiPl | fPsi
compass heading in degrees | float | fLPRho | fLPRho | fRho | fLPRho | fRhoPl | fRhoPl | fRho
tilt angle in degrees | float | fLPChi | fLPChi | fChi | fLPChi | fChiPl | fChiPl | fChi
orientation matrix (unitless) | float | fLPR[3][3] | fLPR[3][3] | fR[3][3] | fLPR[3][3] | fRPl[3][3] | fRPl[3][3] | fRM[3][3]
quaternion (unitless) | Quaternion | fLPq | fLPq | fq | fLPq | fqPl | fqPl | fq
rotation vector | float | fLPRVec[3] | fLPRVec[3] | fRVec | fLPRVec[3] | fRVecPl[3] | fRVecPl[3] | fRVec[3]
angular velocity in dps | float | fOmega[3] | fOmega[3] | fOmega[3] | fOmega[3] | fOmega[3] | fOmega[3] | fOmega[3]
SysTick | Int32_t | SysTick | SysTick | SysTick | SysTick | SysTick | SysTick | SysTick
magnetic inclination angle in degrees | float | N/A | N/A | N/A | fLPDelta | N/A | fDeltaPl | 
Where To Find Things In The Global Structures…
Additional rows available in the Sensor Fusion User’s Guide

## Slide 90: Status Sub-System States
State Name | LED Status | Description
OFF | OFF | The application hasn't started
INITIALIZING | Solid Green | Initializing sensors and algorithms
NORMAL | Blinking Green | Operation is nominal
HARD_FAULT | Solid Red | Nonrecoverable FAULT = something went very wrong.
SOFT_FAULT | Red Flash | Recoverable FAULT = something went wrong, but we can keep going

## Slide 91: Frame of Reference Variations
Item | Aerospace (NED) | Android (ENU) | Windows 8 (ENU)
Axes alignment | XYZ = NED | XYZ = ENU | XYN = ENU
Accelerometer sign | Gravity-Acceleration +1g when axis is down –1g when axis is up | Acceleration-Gravity +1g when axis is up –1g when axis is down | Gravity-Acceleration +1g when axis is down –1g when axis is up
Accelerometer reading when flat | G[Z] = +1g | G[Z] = +1g | G[Z] = –1g
Direction of increasing angles | Clockwise | Counterclockwise | Clockwise
Compass heading  and yaw angle  |  =  |  =  |  = 360°–

## Slide 92: Sensor Drivers
Every sensor driver has at least two functions
  <sensor>_init
  <sensor>_Read
Higher power sensors may also have:
  <sensor>_Idle
The only parameter typically affecting sensor initialization is desired sampling rate. These are set as a function of build.h options at compile time.

## Slide 93: Foundation Functions for Drivers Include:
For I2C:
  Register_I2C_Read()
  Sensor_I2C_Write()
  Sensor_I2C_Read()
For SPI-based devices:
  Register_SPI_Read()
  Sensor_SPI_Write()
  Sensor_SPI_Read()

## Slide 94: Multi-Rate Data Consumption
Physical
Sensor
Sensor Driver
SW FIFO
Fusion Engine
Sensor HW FIFOs fill at the sensor sampling rate
Each river transfers data from HW FIFO to SW FIFO at that driver’s rate
SW FIFOs are emptied at the fusion rate

## Slide 95: Importance of the Hardware Abstraction Layer
Z
X
Y
MMA8451Q
Z
FXAS21002
Z
X
Y
MAG3110
X
Y
Z
X
Y
MMA8451Q
Z
FXAS21002
Z’
X
Y
corrected MAG3110
X
Y

## Slide 96: Core Functions
initSensorFusionGlobals()
installSensor()
initializeFusionEngine()
readSensors()
conditionSensorReadings()
runFusion()
applyPerturbation() (debug only)

## Slide 97: Selecting Your Frame of Reference in board.h
#define NED 0 ///< identifier for NED (Aerospace) axes and angles
#define ANDROID 1 ///< identifier for Android axes and angles
#define WIN8 2 ///< identifier for Windows 8 axes and angles
#define THISCOORDSYSTEM NED ///< Use this one!

## Slide 98: Algorithm Selection Fields in Build.h
Algorithm | build.h control | To Include | To Exclude
Altimetry | F_1DOF_P_BASIC | 0x0100 | 0x0000
Tilt | F_3DOF_G_BASIC | 0x0200 | 0x0000
2D Automotive Compass | F_3DOF_B_BASIC | 0x0400 | 0x0000
Rotation | F_3DOF_Y_BASIC | 0x0800 | 0x0000
Tilt Compensated eCompass | F_6DOF_GB_BASIC | 0x1000 | 0x0000
Gaming Handset | F_6DOF_GY_KALMAN | 0x2000 | 0x0000
Gyro Stabilized Compass | F_9DOF_GBY_KALMAN | 0x4000 | 0x0000

## Slide 99: Sensor Selection Fields In Build.h
Sensor Type | build.h control | To Include | To Exclude
Accelerometer | F_USING_ACCEL | 0x0001 | 0x0000
Magnetometer | F_USING_MAG | 0x0002 | 0x0000
Gyroscope | F_USING_GYRO | 0x0004 | 0x0000
Pressure | F_USING_PRESSURE | 0x0008 | 0x0000
Temperature | F_USING_TEMPERATURE | 0x0010 | 0x0000

## Slide 100: Selecting Sensor Sample Rates and FIFO Sizes in Board.h
#define ACCEL_FIFO_SIZE 32
#define MAG_FIFO_SIZE 16
#define GYRO_FIFO_SIZE 32
#define ACCEL_ODR_HZ
#define MAG_ODR_HZ 200
#define GYRO_ODR_HZ 400
#define FUSION_HZ 40
#define FAST_LOOP_HZ 80
#define OVERSAMPLE_RATE FAST_LOOP_HZ / FUSION_HZ

## Slide 101: Bare Metal Sensor Fusion

## Slide 102: Bare Metal Sensor Fusion - #Includes
// KSDK and ISSDK Headers
#include "fsl_debug_console.h" // KSDK header file for the debug interface
#include "board.h" // KSDK header file to define board configuration
#include "pin_mux.h" // KSDK header file for pin mux initialization functions
#include "clock_config.h" // KSDK header file for clock configuration
#include "fsl_port.h" // KSDK header file for Port I/O control
#include "fsl_i2c.h" // KSDK header file for I2C interfaces
#include "fsl_smc.h"
#include "register_io_i2c.h"
#include "fsl_i2c_cmsis.h"
#include "fsl_pit.h" // KSDK header feile for Periodic Interval Timer
#include "fxas21002.h" // Register and bit-field definitions
#include "mpl3115.h" // Register and bit-field definitions
#include "fxos8700.h" // Register and bit-field definitions
// Sensor Fusion Headers
#include "sensor_fusion.h" // top level magCal and sensor fusion interfaces
#include "control.h" // Command/Streaming interface - application specific
#include "status.h" // Status indicator interface - application specific
#include "drivers.h" // NXP sensor drivers OR customer-supplied drivers
#include "driver_pit.h" // Project-specific, PIT is used to control main() timing loo

## Slide 103: Bare Metal Sensor Fusion – Global Definitions
registerDeviceInfo_t i2cBusInfo = {
.deviceInstance = I2C_S_DEVICE_INDEX,
.functionParam = SMC,
.idleFunction = (registeridlefunction_t) SMC_SetPowerModeWait
};
// Global data structures
SensorFusionGlobals sfg;
struct ControlSubsystem controlSubsystem;
struct StatusSubsystem statusSubsystem;
struct PhysicalSensor sensors[3];

## Slide 104: Bare Metal Sensor Fusion – Initialization in Main()
int main(void)
{
ARM_DRIVER_I2C* I2Cdrv = &I2C_S_DRIVER;
uint16_t i=0;
BOARD_InitPins();
BOARD_BootClockRUN();
BOARD_InitDebugConsole();
I2Cdrv->Initialize(I2C_S_SIGNAL_EVENT);
I2Cdrv->PowerControl(ARM_POWER_FULL);
I2Cdrv->Control(ARM_I2C_BUS_SPEED, ARM_I2C_BUS_SPEED_FAST);
initializeControlPort(&controlSubsystem);
initializeStatusSubsystem(&statusSubsystem);
initSensorFusionGlobals(&sfg, &statusSubsystem, &controlSubsystem);
sfg.installSensor(&sfg, &sensors[0], FXOS8700_I2C_ADDR, 1, (void*) I2Cdrv,
&i2cBusInfo, FXOS8700_Init, FXOS8700_Read);
sfg.installSensor(&sfg, &sensors[1], FXAS21002_I2C_ADDR, 1, (void*) I2Cdrv,
&i2cBusInfo, FXAS21002_Init, FXAS21002_Read);
sfg.installSensor(&sfg, &sensors[2], MPL3115_I2C_ADDR, 1, (void*) I2Cdrv,
&i2cBusInfo, MPL3115_Init, MPL3115_Read);
sfg.initializeFusionEngine(&sfg);
pit_init(1000000/FUSION_HZ);
sfg.setStatus(&sfg, NORMAL);

## Slide 105: Bare Metal Sensor Fusion – Main() Loop
while (true)
{
if (true == pitIsrFlag) {
sfg.readSensors(&sfg, 1
sfg.conditionSensorReadings(&sfg);
sfg.runFusion(&sfg);
sfg.loopcounter
i=i+1;
if (i>=4) {
i=0;
sfg.updateStatus(&sfg);
}
sfg.queueStatus(&sfg, NORMAL);
sfg.pControlSubsystem->stream(&sfg, sUARTOutputBuffer);
pitIsrFlag = false;
}
}
}

## Slide 106: FreeRTOS sensor fusion

## Slide 107: FreeRTOS Sensor Fusion - #Includes
/* FreeRTOS kernel includes. */
#include "FreeRTOS.h"
#include "task.h"
#include "queue.h"
#include "timers.h"
#include "event_groups.h"
// KSDK & ISSDK Headers
#include "fsl_debug_console.h" // KSDK header file for the debug interface
#include "board.h" // KSDK header file to define board configuration
#include "pin_mux.h" // KSDK header file for pin mux initialization functions
#include "clock_config.h" // KSDK header file for clock configuration
#include "fsl_port.h" // KSDK header file for Port I/O control
#include "fsl_i2c.h" // KSDK header file for I2C interfaces
#include "fxas21002.h" // register address and bit field definitions
#include "fxos8700.h" // register address and bit field definitions
#include "register_io_i2c.h"
#include "fsl_i2c_cmsis.h"
// Sensor Fusion Headers
#include "sensor_fusion.h" // top level magCal and sensor fusion interfaces
#include "control.h" // Command/Streaming interface - application specific
#include "status.h" // Sta:tus indicator interface - application specific
#include "drivers.h" // NXP sensor drivers OR customer-supplied drivers

## Slide 108: FreeRTOS Sensor Fusion – Global Definitions
// Global data structures
SensorFusionGlobals sfg;
ControlSubsystem controlSubsystem;
StatusSubsystem statusSubsystem;
struct PhysicalSensor sensors[2];
EventGroupHandle_t event_group = NULL;
registerDeviceInfo_t i2cBusInfo = {
.deviceInstance = I2C_S_DEVICE_INDEX,
.functionParam = NULL,
.idleFunction = NULL
};
static void read_task(void *pvParameters); // FreeRTOS Task definition
static void fusion_task(void *pvParameters); // FreeRTOS Task definition

## Slide 109: FreeRTOS Sensor Fusion – Main() Page 1
int main(void)
{
ARM_DRIVER_I2C* I2Cdrv = &I2C_S_DRIVER;
BOARD_InitPins();
BOARD_BootClockRUN();
BOARD_InitDebugConsole();
I2Cdrv->Initialize(I2C_S_SIGNAL_EVENT);
I2Cdrv->PowerControl(ARM_POWER_FULL);
I2Cdrv->Control(ARM_I2C_BUS_SPEED, ARM_I2C_BUS_SPEED_FAST);
initializeControlPort(&controlSubsystem);
initializeStatusSubsystem(&statusSubsystem);
initSensorFusionGlobals(&sfg, &statusSubsystem, &controlSubsystem);

## Slide 110: FreeRTOS Sensor Fusion – Main() Page 2
sfg.installSensor(&sfg, &sensors[0], FXOS8700_I2C_ADDR, 1,
(void*) I2Cdrv, &i2cBusInfo, FXOS8700_Init, FXOS8700_Read);
sfg.installSensor(&sfg, &sensors[1], FXAS21002_I2C_ADDR, 1,
(void*) I2Cdrv, &i2cBusInfo, FXAS21002_Init, FXAS21002_Read);
sfg.initializeFusionEngine(&sfg);
event_group = xEventGroupCreate();
xTaskCreate(read_task, "READ", configMINIMAL_STACK_SIZE,
NULL, tskIDLE_PRIORITY + 2, NULL);
xTaskCreate(fusion_task, "FUSION", configMINIMAL_STACK_SIZE,
NULL, tskIDLE_PRIORITY + 1, NULL);
sfg.setStatus(&sfg, NORMAL);
vTaskStartScheduler();
sfg.setStatus(&sfg, HARD_FAULT);
for (;;) ;
}

## Slide 111: FreeRTOS Sensor Fusion – read_task()
static void read_task(void *pvParameters)
{
uint16_t i=0; // general counter variable
portTickType lastWakeTime;
const portTickType frequency = 1; // tick counter runs at the read rate
lastWakeTime = xTaskGetTickCount();
while (1)
{
for (i=1; i<=OVERSAMPLE_RATE; i++) {
vTaskDelayUntil(&lastWakeTime, frequency);
sfg.readSensors(&sfg, i);
}
xEventGroupSetBits(event_group, B0);
}
}

## Slide 112: FreeRTOS Sensor Fusion – fusion_task()
static void fusion_task(void *pvParameters)
{
uint16_t i=0; // general counter variable
while (1)
{
xEventGroupWaitBits(event_group, /* The event group handle. */
B0, /* The bit pattern the event group is waiting for. */
pdTRUE, /* BIT_0 and BIT_4 will be cleared automatically. */
pdFALSE, /* Don't wait for both bits, either bit unblock task. */
portMAX_DELAY); /* Block indefinitely to wait for the condition to be met. */
sfg.conditionSensorReadings(&sfg);
sfg.runFusion(&sfg);
sfg.applyPerturbation(&sfg);
sfg.loopcounter++;
i=i+1;
if (i>=4) {
i=0;
sfg.updateStatus(&sfg);
}
sfg.queueStatus(&sfg, NORMAL);
sfg.pControlSubsystem->stream(&sfg, sUARTOutputBuffer);
}
}

## Slide 113: Implementing Fusion Standby Mode

## Slide 114: Fusion Standby Mode
Version 7.xx Sensor Fusion drivers include a <sensor>_Idle() function in some sensor drivers.
It can be used to place affected sensors in a low-power state until the <sensor>_Init() function is called again.
This gives us the basis for implementing a mode of operation in which the application can reduce power during periods of inactivity.

## Slide 115: motionCheck() Function
bool motionCheck(
float sample[3],
float baseline[3],
float tolerance,
uint32_t winLength,
uint32_t *count
)
Returns boolean true if the device appears stationary
sample is a 3-element array containing the processed sensor sample. For accelerometers, these are in units of gravity (gs).
baseline is a 3-element array containing the value to which sample is being compared. If the two arrays do not match within the specified tolerance (the 3rd parameter), then baseline is updated to the current sample value.
tolerance is the amount you have defined to specify the threshold for what you consider a change. The value of tolerance must have the same units as sample and baseline. It also must be above the “noise threshold” of the sensor.
winLength is the number of fusion cycles in which you must see no motion before asserting the “no motion” flag.
count is the number of cycles in which no change has been detected. This tops out at (winLength + 1) to prevent counter overflow.

## Slide 116: main() and read_sensors() are Unaffected
static void fusion_task(void *pvParameters)
{
uint16_t i=0; // general counter variable
float motion_baseline[3] = {0.0, 0.0, 0.0};
bool stationary;
static bool lastStationary;
uint32_t stationaryCount = 0;
while (1)
{
xEventGroupWaitBits( event_group,
B0,
pdTRUE,
pdFALSE,
portMAX_DELAY);
sfg.conditionSensorReadings(&sfg);

## Slide 117: fusion_task() Modifications Continued…
stationary = motionCheck(
sfg.Accel.fGc, // calibrated accel reading
motion_baseline,
0.01,
120,
&stationaryCount);
if (stationary) {
if (!lastStationary) {
FXAS21002_Idle(&(sensors[1]), &sfg);
}
clearFIFOs(&sfg);
} else {
if (lastStationary) { // restart operations
FXAS21002_Init(&(sensors[1]), &sfg);
}
sfg.runFusion(&sfg); // fuse the sensor data
}

## Slide 118: fusion_task() Modifications Completed
sfg.loopcounter++;
i=i+1;
if (i>=4) {
i=0;
sfg.updateStatus(&sfg);
}
if (stationary) {
sfg.queueStatus(&sfg, LOWPOWER);
} else {
sfg.queueStatus(&sfg, NORMAL);
}
sfg.pControlSubsystem->stream(
&sfg,
sUARTOutputBuffer);
lastStationary = stationary;
}
}

## Slide 119: Topics for Another Day

## Slide 120: Topics For Another Day
Storing/retrieving MagCal and sensor trim to/from NVM
The serial communications protocol
Algorithm Topics (Part 2)

## Slide 121: Part 1 Agenda - Review
Sensors 101
What is the sensor fusion library used for?
NXP Sensor Fusion Version 7.00
Supported Hardware and how to get it
Sensor Fusion Toolbox for Windows
Sensor Fusion Toolbox for Android
Supported development tools and how to get them
Using the MCUXpresso Config Tools to generate a Version 7.xx sensor-fusion enabled SDK
Version 7.00 sensor fusion library structure
IDE Road Trip (step out of PowerPoint momentarily)
Various Gory Details
Bare-Metal Implementation
Version 7.00 Build process
Free-RTOS Implementation
Fusion Standby Mode
Topics for Another Day

## Slide 122: The 3-Axis Tilt Algorithm Returns the Same Value for all 4 Variations Below
East
North

## Slide 123: Legend For Couple Slides…
Board-Specific Functions
Sensor-Specific
Generic Functions
run-time installable
functional interface
Legend
time
sequence
Bold black are in-line structures
Bold red are function pointers
Normal text = scalars and pointers

## Slide 124
Application-specific bare metal or RTOS-based main()
install Sensor()
initialize Fusion Engine()
read Sensors()
runFusion()
initSensor FusionGlobals()
<part>_Read()
Status SubSystem
updateStatus()
setStatus()
queueStatus()
Control SubSystem
initializeControlPort()
write()
stream()
control flags
NVMSetBlockFlash()
ApplyMagHAL()
ApplyGyroHAL()
Register_I2C_Read()
Sensor_I2C_Write()
Sensor_I2C_Read()
NXP Sensor Fusion for Kinetis MCUs Verson 7.xx
NonVolatile Storage
Intelligent Sensor SDK
<part>_Init()
Sensor Fusion Core Functions
Physical
Sensor #1 - n
ApplyAccelHAL()
Register_SPI_Read()
Sensor_SPI_Write()
Sensor_SPI_Read()
GPIO
UART
I2C / SPI
Flash Memory
The KSDK is available to main as well
condition Sensor Readings()
initializeStatusSubsystem
Board specific Hardware Abstraction Layer
KSDK = Kinetis Software Design Kit

## Slide 125: 9-axis Accel + Mag + Gyro Complementary Indirect Kalman Filter
Gyro Corrections
Magnetic Compensation
Kalman Filter
The Kalman state vector is composed of:
qg,k orientation error w/r to gravity
qm,k orientation error w/r to magnetic field
b,k error in zero rate gyroscope error
gyro signal
magnetometer
signal
Orientation
Linear Acceleration
Compass Heading
Euler Angles
Accelerometer Corrections
accelerometer
signal
Precision Accelerometer Trim
Magnetic Calibration
Gyro offsets