## Slide 1: Quaternion Math and other Rotation Representations
Michael stanley
NXP Semiconductor Sensors Division
28 April 2017

## Slide 2: Course Outline
Basics Review
Euler Angles
Axis Angle Representations
Rotation Matrices
Quaternions
Final Observations

## Slide 3: Some Basics

## Slide 4: Movement in Space
Any movement from point A to point B can be decomposed into a translation plus optional rotation
We need at least 6 degrees of freedom (DOF) to describe a movement in 3 dimensions: ΔX, ΔY, ΔZ, , θ, Ψ
Ψ
ΔX
ΔY
Roll Pitch Yaw

## Slide 5: Euler’s Theorem
Any two independent orthonormal coordinate frames can be related by a sequence of rotations (not more than three) about coordinate axes, where no two successive rotations may be about the same axis.
- Leonard Euler (1707-1783)
Source: CSE169: Computer Animation Class Notes, Instructor: Steve Rotenberg UCSD, Winter 2005

## Slide 6: There can be multiple, concurrent, frames of reference
North
East
Up
Earth Frame
Body or Device Reference Frame
The device orientation can be defined as the rotation necessary to map the global frame of reference into alignment with the body frame of reference (or vice versa).

## Slide 7: Frames of Reference
Most systems use a Cartesian frame of reference, but which one?
+Y = North
+X = East
+Z = Up
ENU
+Z = Down
+X = North
+Y = East
NED
Aeronautics uses NED
Windows 8 and Android use ENU

## Slide 8: Let’s use a multicolored box for a thought experiment

## Slide 9: There’s more than one way to get from A to B
A
A
B
B

## Slide 10: Rotations Do NOT Commute A followed by B  B followed by A

## Slide 11: There are multiple representations for rotation
Options include:
Euler Angles – intuitive (roll, pitch & yaw), but subject to gimbal lock
Rotation Matrices – rotation as a matrix multiplication
Axis / Angle – easy to understand, difficult to use
Quaternions – similar to axis/angle, with a theoretical background that makes them useful
source: http://en.wikipedia.org/wiki/File:Euler2a.gif
Euler Angle Illustration
axis/angle

## Slide 12: Euler Angles

## Slide 13: Aerospace Frame of Reference (NED)
source: http://www.chrobotics.com/library/understanding-euler-angles

## Slide 14: There are 12 possible sequences
Alpha | Angles | Comments | 
YRP | ψ--θ | Tait-Bryan angles (AKA Nautical or Cardan angles) | All of these are sometimes referred to simply as “Euler Angles”
YPR | ψ-θ- |  | 
PYR | θ-ψ- |  | 
PRY | θ--ψ |  | 
RYP | -ψ-θ |  | 
RPY | -θ-ψ |  | 
RYR | -ψ- | Proper Euler Angles | 
RPR | -θ- |  | 
PYP | θ-ψ-θ |  | 
PRP | θ--θ |  | 
YRY | ψ--ψ |  | 
YPY | ψ-θ-ψ |  | 

## Slide 15: Rotation Polarity
We use the Right Hand System (RHR) to define positive polarity.
The red arrows show positive rotation about each of the three axes.
+Y
+X
+Z
ωz
ωx
ωy

## Slide 16: Euler Intrinsic vs Extrinsic Rotations
Intrinsic rotations are elemental rotations that occur about the axes of a coordinate system XYZ attached to a moving body. Therefore, they change their orientation after each elemental rotation.
Extrinsic rotations are elemental rotations that occur about the axes of the fixed coordinate system xyz. The XYZ system rotates, while xyz is fixed.
We use “Intrinsic” as our standard
Source: Wikipedia

## Slide 17
source: http://science.howstuffworks.com/gimbal1.htm

## Slide 19: Interesting aside…
Gimbal lock is related to the singularities in longitude that you get at the north and south poles
Source: CSE169: Computer Animation Class Notes, Instructor: Steve Rotenberg UCSD, Winter 2005

## Slide 20: Frame of Reference Variations
 | NED | Android | Windows 8
Axes alignment | NED | ENU | ENU
Angle rotation order | Yaw then pitch then roll | Yaw then roll then pitch | Yaw then pitch then roll
Gimbal lock | Roll instability (X-axis) at ±90 deg pitch (Y-axis) | Pitch instability (X-axis) at ±90 deg roll (Y-axis) | Roll instability (Y-axis) at ±90 deg pitch (X-axis)
Roll range | Clockwise1 –180 to 180 deg | Anti-clockwise –90 to 90 deg | Clockwise1 –90 to 90 deg
Pitch range | –90 to 90 deg | –180 to 180 deg | –180 to 180 deg
Yaw range | 0 to 360 | 0 to 360 | 0 to 360
Compass heading | Yaw | Yaw | –Yaw

## Slide 21: Euler Angles are compact and intuitive, but…
Rotation order matters!
There is no simple way to concatenate rotations
There almost as many notations for Euler angles as the references in which they appear. Be specific in your notation.
There may be multiple Euler angle combinations which map to the same physical rotation. They are not unique.
There are typically limits on the range of Euler rotation for each axis (+/- π or +/- π/2), which can lead to discontinuities in representation.
Smooth interpolation between points is problematic.
Euler angles have very poor mathematical properties in comparison with rotation matrices and quaternions, and should be avoided.

## Slide 22: Axis / Angle

## Slide 23: Rotation Vectors and Axis/Angle
Euler’s Theorem also shows that any two orientations can be related by a single rotation about some axis (not necessarily a principle axis)
This means that we can represent an arbitrary orientation as a rotation about some unit axis by some angle (4 numbers) (Axis/Angle form)
Alternately, we can scale the axis by the angle and compact it down to a single 3D vector (Rotation vector)
Source: CSE169: Computer Animation Class Notes, Instructor: Steve Rotenberg UCSD, Winter 2005

## Slide 24
Axis = [X, Y, Z]
Angle = 
origin

## Slide 25: Axis/Angle Representation
Storing an orientation as an axis and an angle uses 4 numbers, but Euler’s theorem says that we only need 3 numbers to represent an orientation
Mathematically, this means that we are using 4 degrees of freedom to represent a 3 degrees of freedom value
This implies that there is possibly extra or redundant information in the axis/angle format
The redundancy manifests itself in the magnitude of the axis vector. The magnitude carries no information, and so it is redundant. To remove the redundancy, we can normalize the axis, thus constraining the extra degree of freedom
Source: CSE169: Computer Animation Class Notes, Instructor: Steve Rotenberg UCSD, Winter 2005

## Slide 26: Rotation Matrices

## Slide 27
Xearth
Zearth
Yearth
Fixed Reference frame = Local Earth Frame
Oe
Xbody
Zbody
Ybody
Ob
Rotating Reference frame = body frame
Consider

## Slide 28
Xearth
Zearth
Yearth
Fixed Reference frame = Local Earth Frame
Oe
Xbody
Zbody
Ybody
Ob
Rotating Reference frame = body frame
Consider

## Slide 29: How does Vector A in the body frame look when viewed from the earth frame?
  Abody = (xb yb zb)T
  Aearth = (xe ye ze)T
Xbody and Ybody are body axes
Xearth and Yearth are local earth axes
A
O
Xearth
Xbody
Yearth
Ybody

## Slide 30: Rotation of Body Frame about Z axis
  xe = xb cos(Y) - yb sin(Y)
  ye = xb sin(Y) + yb cos(Y)
cosY | -sinY | 0
sinY | cosY | 0
0 | 0 | 1
Aearth =
Abody
  Abody = (xb yb zb)T
  Aearth = (xe ye ze)T
Xbody and Ybody are body axes
Xearth and Yearth are local earth axes
R-Z
cosY | sinY | 0
-sinY | cosY | 0
0 | 0 | 1
Abody =
Aearth
RZ
xe
xb
ye
yb
A
O
Xearth
Xbody
Yearth
Ybody
Y
Y
xbcosY
Y
YbsinY
|yb|
Y
ybcosY
xbsinY
Y

## Slide 31: In a similar fashion…

## Slide 32: Stringing these together… and assuming standard NED sequence…
Abody = RNED * Aearth
To translate from body to earth frame, take the inverse of RNED.
The inverse of a rotation matrix is simply it’s transpose.

## Slide 33: For small signals… sin(x)=>x and cos(x)=>1
1 |  | -
- | 1 | 
 | - | 1
=
Very small angle rotations are linear!

## Slide 34: Take the time derivative
1 |  | -
- | 1 | 
 | - | 1
RNED =
0 | z | -y
-z | 0 | x
y | -x | 0
dD(RNED)/dx =

## Slide 35: Application Insight…
Recall:
Abody = RNED * Aearth
If Aearth = [0 0 g]T and/or B[cos b sin]T
where
   is the inclination angle of the magnetic field relative to the horizontal plane
Then you can immediately see the basis for “virtual gyros”
Matrix entries in the derivative relate directly to gyro values

## Slide 36: Quaternions i2 = j2 = k2 = ijk = -1

## Slide 37: Quaternions are Hyper-Complex Numbers
Invented by Hamilton in 1843
Quaternions are a 4-dimensional extension to complex numbers
The first coefficient is a ‘real’ scalar number
The other 3 coefficients form a vector

## Slide 38: Why should we care?
Quaternions provide alternate representation to Euler angles and rotation matrices.
Quaternions are more efficient:
  require less storage
  require fewer math operations
  are not subject to "gimbal-lock"

## Slide 39
Insights:
The quaternion product is not commutative
A multiplicative inverse exists for every non-zero quaternion
We concern ourselves only with quaternions of unit length (i.e. unit quaternions)
Unit quaternions can be used to model rotations
Conventions:
Quaternion denoted by lower case letter:
ex: p or q or r
Bold face letters denote ordinary vectors in R3

## Slide 40: Different ways to write the same quaternion
We can write quaternions as elements of R4:
  q = (q0, q1, q2, q3)
We can also write:
  q = q0 + q, where q = iq1 + jq2 + kq3
OR
q = cos q + u sin q
where :
  u = q1i + q2j + q3k
  u = the axis of rotation
  2q = the rotation about u

## Slide 41: Quaternions are an efficient representation
q = cos q + u sin q
where :
  u = q1i + q2j + q3k
  u = the axis of rotation
  2q = the rotation about u
Versus

## Slide 42: Equality
  If:
    p = p0 + ip1 + jp2 + kp3
    q = q0 + iq1 + jq2 + kq3
  Then p = q if and only if
    p0 = q0
    p1 = q1
    p2 = q2
    p3 = q3

## Slide 43: The Sum of Two Quaternions
  If:
    p = p0 + ip1 + jp2 + kp3
    q = q0 + iq1 + jq2 + kq3
  Then:
  p + q = (p0 + q0) + i(p1+q1) + j(p2+q2) + k(p3+q3)
Addition of two quaternions is commutative:
p + q = q + p

## Slide 44: Multiplication of Quaternion by Scalar
  If:
    c = scalar
    q = q0 + iq1 + jq2 + kq3
Then:
  cq = cq0 + icq1 + jcq2 + kcq3

## Slide 45: The Complex Conjugate of a Quaternion
    If q = q0 + q = q0 + iq1 + jq2 + kq3 , then
        q* = q0 - q = q0 - iq1 - jq2 - kq3
        (pq)* = q*p*
        q + q* = 2 q0

## Slide 46: The norm of a quaternion
the norm of q = length of q = |q|
N(q) = square root of q*q
N(q) = square root of (q02 + q12 + q22 + q32)
The norm of the product of two quaternions = the product of the individual norms

## Slide 47: The Inverse of the Quaternion
q-1 = q* / |q|2
For a unit quaternion: q-1 = q*

## Slide 48: Implications
Taking the inverse of a rotation quaternion inverts the sense of rotation!
You could also get the same effect by inverting just q0
Taken together, these imply that q0 and –q0 model the same orientation!
This can cause problems when interpolating between two quaternions. We solve this problem by selectively inverting a quaternion when the dot product of it with the previous value is less than zero. This forces the “shortest path” between successive quaternions. Alternately, just always force q0 to be greater than zero.

## Slide 49: Refresher: dot & cross products for 3D vectors
If a = (a1, a2, a3) and b = (b1, b2, b3)
Then
a•b = a1b1 + a2b2 + a3b3
The dot is commutative; that is: a • b = b • a
a x b = (a2b3-a3b2)i + (a3b1-a1b3)j + (a1b2-a2b1)k
The cross product is not commutative; that is:
a x b ≠ b x a
=
i | j | k
a1 | a2 | a3
b1 | b2 | b3

## Slide 50: Product of Two Quaternions
The product is not commutative.
pq = p0q0 - p•q + p0q + q0p + p x q
Note that product of two quaternions is another quaternion
scalar
vector

## Slide 51: Vector Representation of Quaternion Product
pq = p0q0 - p•q + p0q + q0p + p x q
Can be expanded to:
p0q1 + p1q0 + p2q3 - p3q2
p0q2 – p1q3 + p2q0 + p3q1
p0q3 + p1q2 - p2q1 + p3q0
pq = p0q0 – p1q1 + p2q2 + p3q3,

## Slide 52: Quaternion Multiplication
Note that two unit quaternions multiplied together will result in another unit quaternion
This corresponds to the same property of complex numbers
Remember that multiplication by complex numbers can be thought of as a rotation in the complex plane
Quaternions extend the planar rotations of complex numbers to 3D rotations in space

## Slide 53: Quaternion Dot Products
The dot product of two quaternions works in the same way as the dot product of two vectors:
The angle between two quaternions in 4D space is half the angle one would need to rotate from one orientation to the other in 3D space
Source: CSE169: Computer Animation Class Notes, Instructor: Steve Rotenberg UCSD, Winter 2005

## Slide 54: Quaternion Rotation Operator
For any unit quaternion
q = q0 + q = cos q + u sin q
and for any vector v Є R3 the action of the operator
Let quaternion v = [0 vx vy vz], then
Lq(v) = w = qvq*
on v may be interpreted geometrically as a rotation of the vector v through an angle 2q about q as the axis of rotation

## Slide 55: Quaternion Rotation Operator
y-axis
x-axis
z-axis
Rotation
Plane
sin(q)
cos(q)
q = Rotation
Axis
q
q
v
w
q = Rotation
Axis
v = a+n
w = qvq*
w = a+m
a
n
v
w
m
2q
Note: v and w are different vectors in left & right representations

## Slide 56: Sequences of Rotations
Suppose that p and q are unit quaternions which define the quaternion rotation operators
Lp(u) = pup* and Lq(v) = qvq*
Then the quaternion product qp defines a quaternion rotation operator Lqp which represents a sequence of operators, Lp followed by Lq. The axis and the angle of rotation are those represented by the quaternion product, r = qp.

## Slide 57: Sequences of Rotations
v = Lp(u) = pup*
w = Lq(v) = qvq* = q(pup*)q*
w = (qp)u(qp)*
w = Lqp(u)
v=Lp(u)
u
w=Lq(v)
Lp
Lq

## Slide 58: Multiple Rotations
IF:
  p and q are unit quaternions and
  we apply rotation based on p then q;
    w = q(pup*)q*
    =(qp)u(qp)*
    = Lqp(u)
So product of qp calculated before rotation function is equivalent to two separate rotations.

## Slide 59: The Quaternion Time Derivative Relates to Angular Velocity…
q(t) = (1/2) q(t) (t)
Where (t) = {0, x, y, z}

## Slide 60: Quaternion to Rotation Matrix
To convert a quaternion to a rotation matrix:
Source: CSE169: Computer Animation Class Notes, Instructor: Steve Rotenberg UCSD, Winter 2005

## Slide 61: Alternate Form
To convert a quaternion to a rotation matrix:
Source: CSE169: Computer Animation Class Notes, Instructor: Steve Rotenberg UCSD, Winter 2005
The diagonals have been changed into an equivalent form

## Slide 62: Rotation Matrix to Quaternion
=
Given:
We can show:
    q0 = (1/2) sqrt(m11+m22+m33+1)
    q1 =(m23-m32)/(4q0)
    q2 = (m31-m13)/(4q0)
    q3 = (m12 – m21)/(4q0)

## Slide 63: Some useful (normalized) quaternions
w | x | y | z | Description
1 | 0 | 0 | 0 | Identity quaternion, no rotation
0 | 1 | 0 | 0 | 180' turn around X axis
0 | 0 | 1 | 0 | 180' turn around Y axis
0 | 0 | 0 | 1 | 180' turn around Z axis
sqrt(0.5) | sqrt(0.5) | 0 | 0 | 90' rotation around X axis
sqrt(0.5) | 0 | sqrt(0.5) | 0 | 90' rotation around Y axis
sqrt(0.5) | 0 | 0 | sqrt(0.5) | 90' rotation around Z axis
sqrt(0.5) | -sqrt(0.5) | 0 | 0 | -90' rotation around X axis
sqrt(0.5) | 0 | -sqrt(0.5) | 0 | -90' rotation around Y axis
sqrt(0.5) | 0 | 0 | -sqrt(0.5) | -90' rotation around Z axis
from: http://www.ogre3d.org/tikiwiki/Quaternion+and+Rotation+Primer&structure=Tutorials#Some_useful_normalized_quaternions
Note: these assume zero value in vector axis used as rotation axis. They are NOT 100% applicable.

## Slide 64: Final Observations

## Slide 65: Suggestions / Comments
Never, never, never use Euler angles for computation purposes
Axis / Angle representations are intuitive when considering angular rate problems, but otherwise best avoided. Use quaternions instead, as they contain similar information.
Rotation matrices have no singularities, but are not as efficient as quaternions.
It’s easy to go back and forth between rotation matrices and quaternions.
Don’t worry about the underlying complexity of quaternion math. Code the subroutines once and just use them.

## Slide 66: Quaternions vs Rotation Matrix Pros & Cons
Topic | Quaternion | Rotation Matrix
Storage | Requires 16 bytes of storage in single precision floating point (4 elements at 4 bytes each) | Requires 36 bytes of storage (9 elements at 4 bytes each)
Computation (for 2 sequential rotations) | 4 elements each requiring 4 multiplies and 3 additions = 28 operations | 9 elements, each requiring 3 multiplies and 2 additions = 45 operations
Vector rotation | Rotating a vector by pre- and post-multiplication of quaternion requires 52 operations | Rotating a vector via rotation matrix requires 15 operations (3 elements each requiring 3 multiplies and 2 additions)
Discontinuities | Generally, we force the scalar part of the quaternion to be positive, which can cause a discontinuity in the rotation axis (it flips). | None
Ease of Understanding | Generally takes a lot of study to understand the details | Easily understood by most engineers

## Slide 67: References
NXP AN5017: Aerospace Android and Windows Coordinate System
NXP AN5022: Quaternion Algebra and Rotations
NXP Sensor Fusion User Guide
Quaternions and Rotations by Jack B. Kuipers
Quaternions, Ken Shoemake, University of Pennsylvania
Rotation Representations and Performance Issues, David Eberly, Geometric Tools, LLC
Representing Attitude: Euler Angles, Unit Quaternions and Rotation Vectors, James Diebel, Stanford University

## Slide 68: Supplementary material

## Slide 69: The following derivation is based upon one found at http://www.euclideanspace.com/maths/algebra/vectors/angleBetween/index.htm
Determining the quaternion necessary to rotate vector V1 into V2

## Slide 70
q = q0 + q = cos q + u sin q (1)
Let f= 2q (2)
q = cos (f/2) + u sin (f/2) (3)
u = V1XV2 / || V1XV2 || (4)
Identity: cos f = V1.V2 / || V1|| ||V2|| (5)
Identity: sin f = 2 sin (f/2) cos (f/2) (6)
sin (f/2) = 1/2 sin f / cos (f/2) (7)
q = cos (f/2) + (1/2 sin f / cos (f/2)) V1XV2 / || V1XV2 || (8)
Multiply by 2 cos (f/2)
2 cos (f/2) q = 2cos2 (f/2) + sin f V1XV2 / || V1XV2 || (9)
Identity: cos f = 2 cos2 (f/2) - 1 (10)
2 cos2 (f/2) = cos f + 1 (11)
2 cos (f/2) q = (cos f + 1) + sin f V1XV2 / || V1XV2 || (12)
Identity: || V1XV2 || = || V1 || || V2 || sin f (13)

## Slide 71
From Prior page
2 cos (f/2) q = (cos f + 1) + sin f V1XV2 / || V1XV2 || (12)
Identity: || V1XV2 || = || V1 || || V2 || sin f (13)
2 cos (f/2) q = (cos f + 1) + sin f V1XV2 / (|| V1 || || V2 || sin f) (14)
2 cos (f/2) q = (cos f + 1) + V1XV2 / (|| V1 || || V2 ||) (15)
substitute (5) into (15)
2 cos (f/2) q = (V1.V2 / || V1|| ||V2|| + 1) + V1XV2 / (|| V1 || || V2 ||) (15)
Multiply everything by (|| V1 || || V2 ||)
2 cos (f/2) (|| V1 || || V2 ||) q = (V1.V2 + || V1|| ||V2||) + V1XV2 (16)
Simplify by renormalizing and we have
q = norm((V1.V2 + || V1|| ||V2||) + V1XV2) (17)

## Slide 72: Averaging Quaternions
Gene Brownd, in "Averaging and Interpolating Quaternions", states that a reasonable estimate of the average of a bunch of quaternions can be obtained by the simple expediant of averaging the components, subject to the following:
  quaternions must be normalized before averaging
  the resulting average must be normalized
  the angles between quaternions should be less than 180°
A more rigorous (and complex) approach is presented by Markley, et. al. in "Averaging Quaternions"

## Slide 73: The Unit Circle
sin=+
cos=+
tan=+
sin=+
cos=-
tan=-
sin=-
cos=-
tan=+
sin=-
cos=+
tan=-
α
α
α
α
0,1
tan=∞
0,-1
tan=-∞
1,0
-1,0
Ψ=α
x=cos(α), y=sin(α)
hyptoneuse=1
Ψ=180-α
x=cos(α), y=sin(α)
Ψ=180+α
x=cos(α), y=sin(α)
Ψ=360-α
x=cos(α), y=sin(α)